Microsoft's: User's Reference for MS-DOS ver3.3
Appendix C, Installable Device Drivers.
══════════════════════════════════════════════════════════════════
ANSI.SYS

The ansi.sys installable device driver lets you use ANSI escape sequences in real mode. An ANSI escape sequence is a series of characters (beginning with an escape character or keystroke) developed by the American National Standards Institute (ANSI).
These sequences are used to define functions for MS-DOS. Specifically, you can change graphics functions and affect the movement of the cursor.

Installing Ansi.sys

To install ansi.sys, include a command line of the following form in your config.sys file:

device=[drive][path]ansi.sys

The escape sequences used in the ansi.sys file are listed in an appendix found at the end of this manual.

ANSI Escape Sequences Used with MS-DOS

This section lists and explains valid ANSI escape sequences for MS-DOS.

The variables listed in the escape sequences themselves are as follows:

The Ansi.sys variables:

  Code	Description
__________________________________________________________________

   Pn	Numeric parameter - a decimal number that you
specify with ASCII digits.

   Ps	Selective parameter - a decimal number that you use
to select a subfunction. You may specify more than
one subfunction by separating the parameters with
semicolons.

   Pl	Line parameter - a decimal number that you specify
with ASCII digits.

   Pc	Column parameter - a decimal number that you
specify with ASCII digits.

The ANSI Escape Sequence List:

 Sequence	Function
__________________________________________________________________

Changing the cursor position:

 ESC[Pl;PcH	Cursor Position (CUP)

 ESC[Pl;PcF	Horizontal & Vertical Position (HVP)

CUP and HVP move the cursor to the position
specified by the parameters. When no
parameters are provided, the cursor moves to
the home position (the upper-left corner of
the screen).

 ESC[PnA	Cursor Up (CUU)

This sequence moves the cursor up Pn lines
without changing columns. If the cursor is
already on the top line, MS-DOS ignores the
CUU sequence.

 ESC[PnB	Cursor Down (CUD)

This sequence moves the cursor down Pn lines
without changing columns. If the cursor is
already on the bottom line, MS-DOS ignores the
CUD sequence.

 ESC[PnC	Cursor Forward (CUF)

This sequence moves the cursor forward Pn
columns without changing lines. If the cursor	is already in the far right column, MS-DOS
ignores the CUF sequence.

 ESC[PnD	Cursor Forward (CUB)

This sequence moves the cursor back Pn columns
without changing lines. If the cursor is
already in the far left column, MS-DOS ignores
the CUB sequence.

 ESC[6n	Device Status Report (DSR)

The console driver outputs an RCP sequence
when it receives the DSR escape sequence.

 ESC[s	Save Cursor Position (SCP)

The console driver saves the current cursor
position. This position can be restored with
the RCP sequence.

 ESC[u	Restore Cursor Position (RCP)

This sequence restores the cursor position to
the value it had when the console driver
received the SCP sequence.

Affecting erase functions:

 ESC[2J	Erase Display (ED)

The ED sequence erases the screen. The cursor
then goes to the home position.

 ESC[K	Erase Line (EL)

This sequence erases from the cursor to the
end of the line (including the cursor
position).

Affecting screen graphics:

 ESC[Ps;...;Psm	Set Graphics Rendition (SGR)

The SGR escape sequence calls the graphic
functions specified by the following numeric
parameters. These functions remain until the
next occurence of an SGR escape sequence.

Graphics Functions

 0	All attributes off
 1	Bold on
 2	Faint on
 3	Italic on
 5	Blink on
 6	Rapid blink on
 7	Reverse video on
 8	Concealed on
30	Black foreground
31	Red foreground
32	Green foreground
33	Yellow foreground
34	Blue foreground
35	Magenta foreground
36	Cyan foreground
37	White foreground
40	Black background
41	Red background
42	Green background
43	Yellow background
44	Blue background
45	Magenta background
46	Cyan background
47	White background
48	Subscript background
49	Superscript background

Parameters 30 through 47 meet the ISO 6429
standard.

 ESC=Psh	Set Mode (SM)
 ESC=h
 ESC=0h	The SM escape sequence changes the screen
 ESC?7h	width or type to one of the following numeric
parameters:

Screen width parameters

 0	40x25 B&W
 1	40x25 color
 2	80x25 B&W
 3	80x25 color
 4	320x200 color
 5	320x200 B&W
 6	640x200 B&W
 7	Wraps at the end of each line

 ESC=Psl	Reset Mode (RM)
 ESC=l
 ESC=0l	Parameters for RM are the same as for SM (Set
Mode), except parameter 7 resets the mode that
causes wrapping at the end of each line.

__________________________________________________________________